## Slide 1: ADDITIONAL HANDOVER BOOKLET
New Opel Astra Electric
ADDITIONAL HANDOVER BOOKLET
June 2023

## Slide 2
What is a BEV?
A BEV (Battery Electric Vehicle) is run exclusively on electricity via on-board batteries that are charged by plugging into an outlet or charging station. These vehicles have no internal combustion engine.
How does a BEV work?
A BEV sees the reduction gear and electric motor utilising the energy stored in the lithium-ion battery pack to deliver strong acceleration and high levels of refinement whilst the integrated on board charger and regenerative braking are utilised to help replenish the battery pack to maximise range, charge times and convenience.
How to recharge the battery?
The battery pack is recharged through the on board charger from an external electricity supply and also through the vehicles regenerative braking system when the vehicle is being driven, maximising range and greatly extending the life of the conventional brake discs and brake pads.
New Opel Astra Electric
OVERVIEW
Strictly confidential document reserved for Opel network internal use
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
1
2
3
4
Key Components
Lithium-ion battery pack
On Board Charger (OBC)
Electric motor
One speed reduction gear

## Slide 3
EXPLORING THE DRIVING POSITION
  INSTRUMENT / INFOTAINMENT / INFO DISPLAYS
  DRIVING MODE
  ELECTRIC DRIVE UNIT
  DRIVING POSITION
  STEERING WHEEL CONTROL
  ACTIVATION / DEACTIVATION OF ADAS
  TOUCH SCREEN
  ON-BOARD COMPUTER
  REGENERATIVE BRAKING (BRAKE MODE)
  DUAL-AREA AUTOMATIC AIR CONDITIONING
  THERMAL PRE-CONDITIONING
  WIRELESS CHARGER
  TOWING CAPACITY
  SMARTPHONE CONNECTION / MYOPEL APP
  TELEPHONE PAIRING
  OPEL CONNECT
  MYOPEL APP
Strictly confidential document reserved for Opel network internal use
Here are the different steps to take with your customer when getting started.
The topics in BOLD are specific to the ASTRA ELECTRIC and are covered in this document.
Other items are described in original booklet
0. REMOVING COVERS
ACCESS TO THE VEHICLE:
  HANDS-FREE ACCESS AND START
  OPENING THE BONNET
  CHILD LOCKS
  OPENING THE TAILGATE
  SENSORS/ CAMERA
  REAR SEAT ISOFIX / FOLDING
  BOOT LAYOUT
DEMONSTRATING CHARGING:
  CHARGING FLAP
  CHARGING CABLES AND TIMES
  PLUGGING IN
  UNPLUGGING
  PROGRAMMABLE CHARGING
STARTING
  IGNITION
  PEDESTRIAN WARNING BUZZER
  EMERGENCY AND ASSISTANCE SERVICES
STEP 0
1
4
3
STEPS 1 to 5
2
5
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
First appointment
ESSENTIAL HANDOVER

## Slide 4
Strictly confidential document reserved for Opel network internal use
ASTRA ELECTRIC
ESSENTIAL HANDOVER SUMMARY
INTRODUCTION
  ASTRA ELECTRIC OVERVIEW 02
  ESSENTIAL HANDOVER SUMMARY 03
  ELECTRIC: ADDITIONAL HANDOVER BOOKLET
DEMONSTRATING CHARGING:
  CHARGING FLAP 05
  CHARGING CABLES 06
  PLUGGING IN 06
  UNPLUGGING 07
  PROGRAMMABLE CHARGING 08
  EXPLORING THE DRIVING POSITION
  INSTRUMENT / INFOTAINMENT / INFO DISPLAYS 09-10
  DRIVING MODE 11
  ELECTRIC DRIVE UNIT` 11
  TOWING CAPACITY 11
  STARTING
  IGNITION 12
  PEDESTRIAN WARNING BUZZER 12
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
First appointment

## Slide 5
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
2
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
CHARGING
CHARGING DEMO
The traction Li-ion (Lithium-ion) battery stores the electrical power of the vehicle. It is installed below the rear seats. The battery range varies depending on the driving type, journey, use of interior temperature equipment and components aging.
CHARGING FLAP OPENING
Show the customer that the charging flap is located on the passenger side of the vehicle.
Have the customer handle the flap opening.
CHARGING FLAP FEATURES
1. Scheduled charge activation button
2. Nozzle lock indicator lamp
If the lamp is red, the nozzle is adequately positioned and secured in the connector.
3. Charging connector
4. Light guides indicating the state of charge
Light Colour | Meaning
White | Welcome light
Blue | Charge on timed
Green flashing | Charging
Green fixed | Charge complete
Red | Malfunction
CHARGING CABLE AND CHARGING TIME
It is possible to charge the battery with several cables.
The charging cable delivered with the vehicle can be used with the power installations in the country of delivery. In case of any stay abroad, check the compatibility of the charging cable with the local power installations.
Contact the Opel network or a qualified workshop to get the appropriate charging cables.

## Slide 6
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
2
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
CHARGING PROCESS
CHARGING CABLE
Invite the customer to take the cable out of the boot.
Show the customer what the control unit is and explain the meaning of the 3 indicator lamps:
POWER :
 Fixed green: POWER
Green: electrical connection established; charging may start.
CHARGE:
 Flashing green: charging in progress or scheduled charging activated.
 Fixed green: charging completed.
FAULT:
If a problem appears or persists with one of the indicator lamps:
Check that the connections are correctly set up and that the electrical equipment has no faults.
If the warning lamp does not go off, contact the network or a qualified workshop.
Note: when connecting the charging cable to the domestic socket, all of the indicator lamps come on for a moment.
Keep the vehicle plugged in during the handover.
Process:
Take the protection lid off the nozzle.
Insert the nozzle in the charging connector.
The start of the charging process is confirmed by the light guides in the flap and the CHARGE indicator lamp in the control unit flashing green.
CHARGING PROCESS
DOMESTIC charging
Connect the charging cable to the domestic socket on the box side. When plugging, all the indicator lamps of the control unit turn on, then the POWER indicator remains fixed green.
Immediate charging is engaged. The nozzle locks in the filler flap (red indicator lamp comes on), if not, it means that the charging process has not started; go back to the beginning of the process by checking that all the connections are accurate.
The light guide turning red in the flap means that the nozzle is locked.
DOMESTIC

## Slide 7
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
2
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
CHARGING MODES
PUBLIC Fast charging (mode 3)
Follow the use instructions of the fast-charging box.
Take the protection lid off the nozzle.
Insert the nozzle in the charging connector.
The start of the charging process is confirmed by the light guides in the flap flashing green, if not, it means that the charging process has not started; go back to the beginning of the process by checking that all the connections are accurate. The light guide turning red in the flap means that the nozzle is locked.
Note: once charging has started, the calculation of the charging time appears in the control unit (may take up to 20 seconds). Such information disappears when the vehicle is dead locked and an update is available each time it is unlocked.
Disconnection
Before disconnecting the charging connector nozzle:
If the vehicle is unlocked, lock it then unlock it.
If the vehicle is locked, unlock it. The red light guide turning off in the flap confirms that the charging nozzle is unlocked.
Disconnect the charging nozzle within 30 seconds.
PUBLIC Direct DC charging (mode 4)
Follow the use instructions of the fast-charging box .
It is the direct current charge up to 200A, 400V. With this system it is possible to recharge the vehicles in a few minutes, the charger is external to the vehicle and the cable directly to the charging station
Cable mode 3 (as accessory)
DOMESTIC charging (mode 2)
The end of charging is confirmed by the CHARGE LED turning fixed green on the control unit and by the light guides turning fixed green in the flap.
After disconnecting, put the protection lid back on the nozzle and close the charging flap.
Disconnect the charging cable to the domestic socket on the box side.
Cable mode 2 (standard)
DOMESTIC Universal charger (mode 2 and mode 3)
The universal charger allows charging with different kind of sources
It is compliant to charging currents from 1.8A up to 22A and offers different adapters for the different sockets.
Universal charger (as accessory)
DOMESTIC
PUBLIC

## Slide 8
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
2
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
CHARGING
PROGRAMMABLE CHARGING
By default, charging starts as soon as the nozzle is connected. Scheduled charging may be programmed.
Explain that Programmable charging is only possible when charging at a domestic electrical outlet or a reeinforced/ Green'Up socket or a wall box.
Programmable charging is also available via the MyOpel App.
Setting the wanted charging time on the touchscreen
Activation
Select charging
Define number of hours and minutes of charging required
Touch OK
Plug in the vehicle
Within one minute press
Status indictaor illuminates blue to show that programmable charging is active
CHARGING TIMES (20 – 80%)
DOMESTIC socket | DOMESTIC Wall Box | PUBLIC AC charger | PUBLIC DC charger
Mode 2 cable | Mode 3 cable | Mode 3 cable | Fixed DC cable
2.2kW => 15h50 | 7.4kW => 4h40 | 22kW => 3h10 | ≥100kW => 26m
Reinforced socket 3.2kW => 11h10 |  |  | 

## Slide 9
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
Have the customer operate the controls of the head-up display and explain the features and the ability to add a personalised widget.
Show the various displays within the instrument cluster and Driver Info Display, pointing out that the flows relate to the driving modes and the colours relate to the driving situation:
Blue = electric driving
Green = energy recovery
3
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
  INSTRUMENT / INFOTAINMENT / INFO DISPLAYS
Motor stopped
Motor on
Vehicle accelerating

## Slide 10
Handover agent
Customer
STEP
Strictly confidential document reserved for Opel network internal use
3
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
INSTRUMENT / INFOTAINMENT / INFO DISPLAYS
Vehicle braking
Show the customer the graph that highlights electricity consumption, detailing:
Average power consumption (kWh/100km) on current trip and historical figures
Energy consumed from the traction battery – blue graph
Energy regenerated during deceleration and braking to replenish battery – green graph
Opel Connect
Explain that energy consumption data is available remotely via the “MyOpel” app.
Show the new Opel Connect feature of EV Trip Planner that is newly available.

## Slide 11
Towing Capacity
Explain that Astra electric has the capacity to tow up to 80kg
Driving Modes
Explain to the customer the driving modes and how they are differentiated from each other:
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
New Opel Astra Electric
DRIVING MODES / ELECTRIC DRIVE UNIT
Handover agent
Customer
STEP
3
P – this position locks the wheels, to shift out the brake pedal should be depressed and the desired mode selected. P is automatically selected when drivers door is open and speed is less than 5 km/h and when ignition is switched off.
R – denotes reverse and can only be selected when vehicle is at a standstill and brake pedal is depressed.
ECO – when wanting to maximise efficiency / range. Power limited to 80kW, HMI feedback and climate control is set to ECO mode.
NORMAL – default setting for good balance between efficiency / range and other vehicle functions. The power is limited to 100kW and the vehicle reverts to NORMAL on start up.
SPORT – to maximise driving enjoyment. Power steering weight increases, HMI feedback is maximised and the available power is maximum of 115kW .
Important: Being in ECO or NORMAL mode and using the kick down function the engine always deliver the max. power of 115kW. Releasing the gas pedal the vehicle automatically switches back to the original mode.
Electric Drive Unit
EXPLAIN that the vehicle uses an electric drive unit with a 1 gear transmission.
Show the positions and explain that the selector will always return to the centre position.
N – neutral and no power can be transferred to the front wheels.
D – This mode is for normal driving. To shift into and out of D, the vehicle must be at standstill and the brake pedal has to be depressed.
B - vehicle speed is significantly reduced by releasing the accelerator pedal without operating the brake pedal. Use B when driving down steep hills, in deep snow, in mud or in stop-and go traffic. To activate B, select D and press button B To deactivate B, press button B.
Strictly confidential document reserved for Opel network internal use

## Slide 12
ADDITIONAL HANDOVER BOOKLET ASTRA ELECTRIC
Ignition
Press the brake pedal fully.
Keep your foot on the pedal.
Press the START/STOP button for approximately 2 seconds.
Keep the brake pedal depressed until READY is displayed in the Driver Information Centre and an acoustic signal is given.
Pedestrian Warning Buzzer
Explain that the system warns pedestrians of the vehicle's arrival when it is running..
The audible pedestrian warning system operates as soon as the vehicle is set in motion and up to 30 km/h, both forward and reverse.
New Opel Astra Electric
STARTING
Handover agent
Customer
STEP
3
Strictly confidential document reserved for Opel network internal use

## Slide 13: Thank you